## Slide 1
How to Maintain
SAFELY
Landscape at Height?
Philippe Girardot
Founder of Akrobat Pte Ltd
Sustainable Landscape
Design conference on 3rd March 2017

## Slide 2
I/ Specificities of landscape maintenance
II/ New Architectural Challenges
-> Hazardous accesses with a risk of fall
Terraces
Planters at the edges
Vertical walls
Slopes
Steel trees ……
III/ Fall arrest Solutions implemented in Singapore
Gardens by the Bay
Changi International Airport planters
Singapore Zoo and Jurong Bird Park
Outside greeneries : condominium
Sustainable Landscape
Design conference on 3rd March 2017

## Slide 3
Pruning - Watering…
Weekly – monthly basis
Hand free system
I/ Specificities of landscape maintenance
a) Plants & trees need a regular maintenance
System must be EASY to use
by non specialists at height

## Slide 4
b) Plants & trees grow
I/ Specificities of landscape maintenance
Lifeline

## Slide 5
I/ Specificities of landscape maintenance
c) aesthetic

## Slide 6
d) waterproofing
I/ Specificities of landscape maintenance
e) Soil : soft support

## Slide 7
II/ New Architectural Challenges
-> Hazardous accesses with a risk of fall
a) Terraces

## Slide 8
II/ New Architectural Challenges
b) Planter at the edge

## Slide 9
II/ New Architectural Challenges
c) Green wall
d) Roofs
c) Other fanciest…

## Slide 10
Lifeline
  Wall, Parapet, RC roof
  Metal roof without penetration
  Overhang / mixed lifeline : Zoo, Bird Park, Garden by the Bay
Anchor points
  conventional
  Custom made : ground anchor, circling, davits
  Deadweight anchors
Overhang Monorail
  With SRL
  With ladders & attachment from ground
  For Rope access – option rope climber – vertical green walls
Gantries : traveling Ladders
III/ FALL ARREST SYSTEMS PROPOSED IN SINGAPORE

## Slide 11
Planters – Lifeline systems
PRINCIPLE :
Wire lifeline Fixed on RC wall
Use of a Normal lanyard
Worker secure himself before climbing over the wall
III/ FALL ARREST SYSTEMS PROPOSED IN SINGAPORE

## Slide 12
Planters – Terraces : LIFELINE
RC walls
Strong structure
III/ FALL ARREST SYSTEMS PROPOSED IN SINGAPORE

## Slide 13
Planters / terrace
LIFELINE on RC parapet
III/ FALL ARREST SYSTEMS PROPOSED IN SINGAPORE
PRINCIPLE :
Wire lifeline Fixed on RC wall
Use of an adjustable lanyard
Worker secure himself before climbing over the wall
Passing through from distance

## Slide 14
Soil …Lifeline at proper height
Adjustable lanyard
LIFELINE
Lifeline
Lifeline
Installation without soil & plants
III/ FALL ARREST SYSTEMS PROPOSED IN SINGAPORE

## Slide 15
Adjustable lanyard
LIFELINE on RC parapet
LIFELINE WITH HIGH POSTS - GBTB
III/ FALL ARREST SYSTEMS PROPOSED IN SINGAPORE

## Slide 16
3 years later…
Lifeline
Lifeline
LIFELINE WITH HIGH POSTS GBTB
III/ FALL ARREST SYSTEMS PROPOSED IN SINGAPORE

## Slide 17
Lifeline, anchors 1.5m higher….
LIFELINE WITH HIGH POSTS - GBTB
III/ FALL ARREST SYSTEMS PROPOSED IN SINGAPORE

## Slide 18
LIFELINE
WITH HIGH POSTS
III/ FALL ARREST SYSTEMS PROPOSED IN SINGAPORE

## Slide 19
Lifeline, anchors higher….
LIFELINE WITH HIGH POSTS
III/ FALL ARREST SYSTEMS PROPOSED IN SINGAPORE

## Slide 20
Special brackets
No drilling of the waterproofing layer
III/ FALL ARREST SYSTEMS : Roof RC

## Slide 21
Precinct pavilion punggol
LIFELINE ON METAL ROOF – clamping
Clamped Spider lifeline
No roof penetration
III/ FALL ARREST SYSTEMS : Metal Roof

## Slide 22
Sentosa Beach bridge
III/ FALL ARREST SYSTEMS : Metal Roof
LIFELINE ON METAL ROOF – clamping
Clamped Spider lifeline
No roof penetration

## Slide 23
Sentosa Beach bridge
III/ FALL ARREST SYSTEMS : Metal Roof
LIFELINE ON METAL ROOF – clamping

## Slide 24
No penetration - waterproofing
No clamping - Dead weight fixing
LIFELINE ON METAL ROOF – dead weight
III/ FALL ARREST SYSTEMS : Metal Roof

## Slide 25
AFTER
LIFELINE ON METAL ROOF – dead weight
III/ FALL ARREST SYSTEMS : Metal Roof

## Slide 26
LIFELINE – Leaves on roof
Overhang lifeline
III/ FALL ARREST SYSTEMS

## Slide 27
LIFELINE – Leaves on roof
III/ FALL ARREST SYSTEMS

## Slide 28
Anchors – for slopes
Deadweight fixed
III/ FALL ARREST SYSTEMS

## Slide 29
Anchors for slopes
Custom made ground anchors : GBTB. Condos…
III/ FALL ARREST SYSTEMS

## Slide 30
Overhang monorail
With use of SRL
Less deflection
Better traveling
III/ FALL ARREST SYSTEMS

## Slide 31
Anchors Fixed by cercling
Anchors for steel trees
GBTB Super trees and Changi International Airport
III/ FALL ARREST SYSTEMS

## Slide 32
Telescopic pole with carabiner
Anchors for steel trees
Attach the carabiner and the vertical lifeline to the anchor
Climb safely with ladder fixed and secured to the vertical lifeline
III/ FALL ARREST SYSTEMS

## Slide 33
Overhang monorail with ladders
III/ FALL ARREST SYSTEMS
Safe way to prune vertical walls

## Slide 34
Step 1
Attach the vertical lifeline from the floor
Overhang monorail with ladders
Step 2
Attach the ladder to the track by its hooks
Step 3
Climb safely with ladder fixed and secured to the vertical lifeline
III/ FALL ARREST SYSTEMS
Principle

## Slide 35
Aluminium track
Coloured
Vertical walls : Overhang monorail for rope access
Curve along the vegetal wall
III/ FALL ARREST SYSTEMS

## Slide 36
Use with motorized rope climber
Vertical walls
Overhang monorail
for rope access
III/ FALL ARREST SYSTEMS

## Slide 37
Traveling ladders fixed to gondola track
III/ FALL ARREST SYSTEMS

## Slide 38
THANK YOU
FOR YOUR ATTENTION